## Slide 1: Human BODY as Data Transmission Medium
Author: Juris Ormanis
Juris.Ormanis@edi.lv
Supervisor: Modris Greitāns

## Slide 2: Objectives
Develop Human body signal transmission model
Characterize Human body from the communication channel point of view
Describe skin contamination influence on channel parameters

## Slide 3: Introduction
Market growth by 210% in next 4 years [https://www.statista.com/]
In 2021 number of wearable devices will reach 500 million units
Notes: As timely prevention, monitoring and feedback are recognized to reduce medical expenses and improve outcomes, wearable sensor systems are becoming more and more prevalent. The forecast for next 4 years is that market of wearable medical electronics will grow by 210%, and the number of wearable devices in the world will reach 500 millions. It is around 7-9 devices per user

## Slide 4: Challenges in body sensor network area (BSN/BAN)
Easy wearing/using
Throughput limitation
Privacy and security
Energy efficiency
Notes: According to such significant grow, we should prepare for this. We could define following challenges for body sensor networks.
Easy wearing/ usability
Throughput limitation
Privacy and security
And energy efficiency

## Slide 5: Body coupled communication
Privacy and security as well as using wires
Easy to wear as wireless devices
Your body is your private transfer medium
Energy efficient
Wearable devices
Communication link
Notes: There were a few attempts to overcome previously mention problems using radically different technology. One of them was Body coupled communication (BCC), also known as intrabody communications (IBC). This means that the nodes on the wearable sensor network use the body of the wearer itself as the medium for communication.
BCC provides privacy and security level like wired communication
Devices that uses these technology are easy to wear and they does not limit everyday activities
Your own body becomes data transfer medium, so you don’t need to share you data link with other devices
And it is very energy efficient. Speaking about power consumption data transfer using Bluetooth low energy protocol consummates about 25miliwatts, so the Body coupled communication consumes about 5micro watts

## Slide 6: Safety
~300μA
Notes: As to we are trying to apply some electrical signals to the human body, we should be sure that it will not harm people. In table we could see that According to IEEE standard the maximum current that could be applied to human person should not overcome half of miliamper for frequencies till 3 khz, 200mA fro frequencies till 100khZ and 50mA for frequencies till 110mhz. The currents in our experiment is more that 1000 times smaller, so that could not harm people in any way.

## Slide 7: Setup
Side A
Notes: As was mention before, many papers show that it is possible to transfer data through the body, but in these papers most common wireless modules are used. I mean that researchers are using 10mhz 100mhz 433mhz 2.4ghz transmitting modules and connect their antennas outputs to the skin. That gives us practical answer that intrabody communication is possible, but in this paper we wanted to find an answer on which frequency should we transmit our data.
For experiments two conductive bands were made. On the picture you could see schematic of 2 sides of the band and the photo of the band. To ensure signal source contact with the body, generator leads connects to the conductive textile. Each of two bands should be worn on participant

## Slide 8: Frequency response of the bands

## Slide 9: Results – Human Body Frequency Response

## Slide 10: Validation

## Slide 11: Validation results

## Slide 12: Results

## Slide 13: Results - Experiment schematic

## Slide 14: Results – Wrist Impedance

## Slide 15: Results – Human body frequency response
Notes: As the result we could see the obtained data in form of bode plot or frequency response. On the figure is the average value from 10 data sets. As you already noticed there exist two points of interest, one is at frequency about 3.2 MHz and second at frequencies about 10MHz. Using linear analysis tool from Matlab we could construct following equation

## Slide 16: Results – Model

## Slide 17: Results – Model adjusting

## Slide 19: Results – Channel parameters
ΔF | 1MHz
Fc | 3.25MHz
Attenuation | −22dB÷−25dB
SNR | 16.9dB
Impedance at Fc | 120Ω

## Slide 20: Results – influence of skin contamination on FR

## Slide 21: Next steps
More measurements
Identify the relationship between the location of the electrodes and the output power
Find optimal signal power to ensure high SNR but minimize the signal interference on/from other users

## Slide 22: Thank you for attention